## Slide 1: Commercial Shipping
Scheduling, Routing & Bunkering Unit #5

## Slide 2: Importance of Scheduling & Routes
In planning a vessel’s sailing schedule it is of the utmost importance that it be fully employed while it is available.
It earns no money for the shipowner when laid up – whether for survey, general maintenance, or due to lack of traffic.
Such periods must be kept to an absolute minimum. This is important because of the large amount of capital invested in a ship, which has heavy annual depreciation charges.
A ship must earn as much profit as possible during its limited life.

## Slide 3: Tramps & Cargo Liners
For the commercial aspects of shipping, there are clear lines of division in the operation of vessels.
Tramp shipping does not operate according to any published schedule neither is it constrained by practice. It will however operate according to a particular demand.
Liner shipping however, sails on fixed schedules which are advertised in the public domain for the benefit of shippers. The route is also made available.

## Slide 4: Factors influencing sailing schedule
traffic and competition – volume/type/seasonality
available ships – size/special equipment/plying limits
crew availability and certification – cost/available
efficiency of ship and port operations – time margins/port efficiency and service/voyage time/cost/traffic
uncontrollable conditions of work – climatic/hostility/flag discrimination/canals/tidal effect/conference agreements

## Slide 5: Load Lines Convention
It has long been recognized that limitations on the draught to which a ship may be loaded make a significant contribution to her safety.
These limits are given in the form of freeboards, which constitute, besides external weathertight and watertight integrity, the main objective of the Convention.
The amount of cargo and supplies that may be carried on board a vessel varies with the route followed and the time of the year.
This is because the maximum permitted draft varies according to the season and waters in which the vessel plies.

## Slide 6: Load Lines Convention
The first International Convention on Load Lines, adopted in 1930, was based on the principle of reserve buoyancy, although it was recognized then that the freeboard should also ensure adequate stability and avoid excessive stress on the ship's hull as a result of overloading.
In the 1966 Load Lines convention, adopted by IMO, provisions are made determining the freeboard of ships by subdivision and damage stability calculations.
The regulations take into account the potential hazards present in different zones and different seasons.

## Slide 7: Load Lines Convention
The main purpose of these measures is to ensure the watertight integrity of ships' hulls below the freeboard deck.
All assigned load lines must be marked amidships on each side of the ship, together with the deck line.
Ships intended for the carriage of timber deck cargo are assigned a smaller freeboard as the deck cargo provides protection against the impact of waves.
Loadlines define the minimum amount of freeboard the vessel must have.
Freeboard is the distance measured amidships from the water line to the uppermost continuous deck in a ship with one or more decks.

## Slide 8: Loadlines
The navigable waters of the world are divided into loadline zones defined by the International Convention on Load Lines (1966).
These geographical areas are described as either tropical (T), summer (S), or winter (W).
Some areas are permanent and others are seasonal.
When a ship is loaded to its tropical loadline mark, the ship’s master must take care that a seasonal tropical zone does not change to summer whilst the vessel is trading there. In such a case, the summer mark would be submerged and the ship would be overloaded and illegal.

## Slide 9: Loadlines
Also, as the vessel crosses from a tropical to an adjacent summer zone, the ship’s master must ensure that the weight carried is reduced enough to ensure that the ship rises in the water to its summer mark.
This is done through the vessel’s consumption of the correctly estimated amount of bunkers and water. Similar constraints apply, of course, for a ship moving from a summer to a winter zone.
The safety and security of life at sea, protection of the marine environment and over 90% of the world's trade depends on the professionalism and competence of seafarers.

## Slide 10: Choice of Bunkering Ports
During a voyage, bunkers and water are continually used. Sufficient bunkers and water must be carried for each leg of the journey, but this must be balanced with the need to maximize revenue-producing cargo.
Overall weights that can be carried are limited by the need to respect legal load lines that depend on the location and season.
There is no hard and fast rule about where bunkers should be replenished. It is in the shipowner’s interest to run each voyage as efficiently as possible, minimizing time and costs while maximizing revenues.

## Slide 11: Choice of Bunkering Ports
With sustained high bunker prices and the increasing attention on green shipping, how to choose the optimal bunkering ports for saving total operating costs and minimize fuel emissions are research issues arising in the liner shipping companies.
Generally speaking, the bunkering port selection problem is solved by ship planning software, which can only work optimally when the ship arrivals can be forecasted rather accurately, but ignoring some unforeseen circumstances in actual operations.

## Slide 12: Choice of Bunkering Ports
There are no fixed rules for the bunkering port selection among several alternatives yet.
This is addressed by benchmarking that evaluates the bunkering ports’ performance under the regular liner route to choose the optimal ones.
Owing to bunkering port selection is typically a multi-criteria group decision problem, and in many practical situations, decision makers cannot easily express their judgments under an incomplete and uncertain information environment with exact and crisp values.

## Slide 13: Factors affecting ports
Load line restrictions
Draft restrictions in ports
Price of bunkers
Freight rates
Types of cargo
Port charges
Delays/productivity(loading rate)

## Slide 14: Determining factors
In general, reserves are essential for a long voyage, and a bunker call should:
avoid deviation from the route
avoid high costs (fuel and port charges)
take no more than half a day.
Calculations must be made to decide when and where to bunker.